## Slide 2: MBGNet Short Term Survival Kit
What you need to know for a SHTF scenario while MF is away.

## Slide 3: Diagnostics
If something is not working with a server, try to SSH into it.
If not responsive by SSH, see if it is powered on. (This is why they ask you if things are plugged in when you call any helpdesk.)
If powered on, see if you can communicate to it some other way. You might need to reboot.
If powered off, determine why the power is off. There are numerous possibilities.

## Slide 4: Hypervisors
Ekkaia (VMware)
Helkar (VMware)
Belegaer (VMware)
Nurnen (KVM)
Leaflock (KVM) These are all in the partslist.org domain DNS. All run a version of CentOS. You may ssh to them and/or connect to them via KVM-over-IP. All are in JWG 372.

## Slide 6: To get into Vmware HyperVs
Kvmg.gersteinlab.org
Log in
Click on the HyperV
Troubleshoot Note: there is a command line based way of doing this. That is, one can SSH directly to the hyperV and issue commands.

## Slide 9: VMware hosts
Logged in as root.
VMware (workstation) running. Hosts that are intended to be on are in the Favorites list.

## Slide 11: To get into KVM HyperV
ssh -X root@<hypervisor>.partslist.org
virt-manager
Troubleshoot Note: there is a command line way of doing this. That is, one can SSH directly to the hyperV and issue commands.

## Slide 13: KVM hosts
VMs run in the background
KVM is an industry grade hyperV
VMs come up during reboot.

## Slide 14: Physical Machines
Anduin.mbgnet/anduin.mbb.yale.edu Router
Minas-tirith/morgul/anor/ithil Powervault disk controllers
Procurve switches Turn these off and everything goes down

## Slide 15: Physical Machines (cont’d)
Netapp NAS and Dell Powervaults File shares
UPSs Newly upgraded

## Slide 16: MBGNet Virtual Network Infrastructure
Gondor.mbgnet (central mount point)
Isildur.mbgnet (NIS)
Valinor.mbgnet (DHCP)
Araman.mbgnet (NIS/DHCP backup) These all sit in Nurnen.

## Slide 17: Amazon EC2
Papers/Lectures
Info/WWW To access these, you ssh using your ssh key. The good: administering is easy. The bad: administering is limited.

## Slide 18: How to contact MF
Email: mihali.felipe@yale.edu
Skype: mihalifelipe
Will give phone number in PH when he gets there.
Telepathy