## Slide 1: Genome Sequencing Technical Issues
Genome Sequencing Program Steering Committee Teleconference
11/17/17

## Slide 2: Sequencing Technology Working Group
Created to share information on development activities
  Originally formed between BCM, WU-MGI, and The Garvan Institute
    Development of the HiSeq X Platform – Focus now shifted to NovaSeq and some 10X Genomics
  Expanded to all CCDG sites Early 2016
Goals
  Provide a mechanism to share ideas/issues to shorten development cycle of new technologies
    Enable rapid identification of potential reagent/platform issues independent of vendors
    Provide interface with industry partners to shape development priorities and standards
  Engaged with Illumina
    Had face to face at ASHG 2017
    Planning quarterly phone calls with Illumina
    Planning face to face technical summit
    Illumina has expressed interest in engaging our group in general as we’re key to their development

## Slide 3: NovaSeq Development
NovaSeq 6000
  2 X 150 bp in ~40 hours for S2 flow cell - >1Tb/FC
  S4 FC recently released (10/17) with >3Tb/FC in ~40 hrs
  Advantages of NovaSeq
    Automated on board cluster gen, cassette loading for ease of loading, loading pool to denaturation to load in 15 Min, two flowcells that are completely independent of each other, automatic post run wash
    Open to WGS, WES, Targeted Sequencing, and RNAseq

## Slide 4: NovaSeq Development
Active development at all CCDG sites
  Platform challenges
    Patterned flow cell issues
      Duplication rates
      ExAmp/Index switching contamination (alleviated by some dual indexing schemes)
      Reduced quality index reads
        Alleviated by alternative sequencing protocol
    Huge flow cell capacity and reduction of granularity of flow cell
      S4 flow cell = >3Tb = >33 - 30X WGS samples = 300-600 WES
      S2 flow cell = >1Tb
      Lane loader in development at Illumina to provide 2-4 independent lanes - $2K for device but $800-$1000 list price for disposable for each flow cell. Increased loading times and manual intervention

## Slide 5: NovaSeq Development
Sample Indexing
  Currently 24 dual unique Illumina supported indexes available with 96 by end of 2017/early 2018.
  384 indexes for PCR only protocol available 2018.
  Other indexing available or in development independent of Illumina
Sample Pooling
  HiSeq X – Wash U – Pools of 24 WGS samples – Titration run (typically 4 lanes), Primary run (16 lanes) – Final top-up for pools of samples if necessary
  NovaSeq
    In development
    Potentially involving different data types – WGS, WES, RNA seq
    Indexing schemes critical
Similar Quality to HiSeq X
  Comparisons are underway of quality and variant calling results
  All indications thus far suggest similar quality

## Slide 6: SNP Concordance: NIST Standard NA12878
96.18%
3.41%
0.41%
NovaSeq NA12878 (36X) vs NIST
0.88%
NovaSeq NA12878 (36X)
vs
HiSeq X NA12878 (37X)
2.67%
0.37%
HiSeq X NA12878 (37X) vs NIST
96.95%
0.98%
98.11%
Both platforms have >96% overlap to the NIST NA12878 standard.
A direct comparison of SNP calls from the two platforms were found to be highly concordant (98.11%) and typical of technical replicates on the same platform. (Comparison limited to NIST high confidence calls)
(Comparison data: BCM-HGSC)

## Slide 7: OMIM Gene Coverage (100% at ≥20X) vs Mean Coverage
Chart: Titrated Mean Coverage
| 25.57 | 30.38 | 35.1
NovaSeq - HS1011 | 493 | 1444 | 2494
NovaSeq - NA12878 | 674 | 1824 | 2861 | 3376 | 3520 | 3554 | 3571
NovaSeq - NA12878 | 475 | 1445 | 2500
NovaSeq - NA19238 | 531 | 1597 | 2722 | 3324 | 3525 | 3555
NovaSeq - NA12892 | 475 | 1603 | 2793 | 3366 | 3516 | 3566 | 3581 | 3592
NovaSeq - NA12891 | 584 | 1554 | 2551 | 3130
NovaSeq - NA12878 | 666 | 1667 | 2718 | 3323 | 3511
NovaSeq - HS1011 | 486 | 1605 | 2635 | 3185 | 3334 | 3377
HiSeq X - NA12878 | 448 | 1864 | 3070 | 3487 | 3561 | 3581 | 3586 | 3591 | 3595 | 3599 | 3600
HiSeq X - NA19238 | 979 | 2386 | 3244 | 3495 | 3560 | 3582 | 3590 | 3596 | 3602 | 3606 | 3607
Number of Genes 100% at ≥ 20X
Similar performance shown between platforms when comparing coverage of clinically relevant genes
(Comparison data: BCM-HGSC)

## Slide 8: 10X Genomics Overview
(Church 10X Genomics)

## Slide 9: 10X Genomics Phasing – Important for Het vs. Repeat Copy Resolution
(Church 10X Genomics)

## Slide 10: 10X Genomics Development
Advantages
  Can make a library with 1ng inputs
  Provides long phasing information (Mbs)
  Provides long linking information – enables enhanced read mapping in repetitive regions of the genome
  Enhanced SV detection
Disadvantages
  $$$ - ~5-10 times more expensive than standard short read library
    ~1.5X more expensive than standard short read sequencing
  PCR based strategy so has more biases than PCR-free libraries
  Requires high molecular weight DNA for optimal performance
Example Application
  WU CCDG development project
    Utilize 10X genomics to identify (& phase) variation in regions not interpretable from short reads alone
    Develop methods to genotype and/or impute variants using other data types (standard WGS or genotype data)
    Samples: diverse populations, GRU consents
    Leverage high quality genome assemblies from other projects (i.e., Genome Reference, 1000 Genomes, Genome in a Bottle)

## Slide 11: Other Sequencing Development
PacBio Sequel – Long read data production
  Average read lengths >12-13kb with N50 read lengths >20kb
  ~20 times more expensive per base than short reads
  Typically requires more coverage than short read data
  High error rates (10-15%)
  Requires micrograms of DNA for library construction
  New reports indicate confirmation of 80% of known SVs with 10-15x coverage
Oxford Nanopore – Long read data production
  Similar if not greater lengths than PacBio
  Similar cost model
  Similar error rate, although a bit more systematic
  DNA input requirements are ~10x more than PacBio
  Performance - greater run-to-run variability

## Slide 12: Proposed CCDG Joint Technical Pilot
Current CCDG Tech Dev Proposals
  Similar technology development cycles at each CCDG site.
  Similar proposals to incorporate new long-range technologies to WGS to achieve comprehensive genomes.
  Other groups already achieved technical demonstration: Chaisson, M., et al bioRxiv, 2017. https://www.biorxiv.org/content/biorxiv/early/2017/09/23/193144.full.pdf
Joint Technical Pilot
  Aim to identify new disease associations with CNVs, SVs, and haplotype phasing methods not in play using standard WGS/WES.
  Coordinate plans to generate long-read data across centers, cohorts, ethnic groups, target phenotype/disease.
  Collaborate with Analysis Centers for new imputation methods.
  Collaborate with Data Working Group to improve variant calling.
  Develop a pilot plan for coordination to achieve above aims across centers.