Normal Modes for predicting protein motions: A comprehensive database assessment and associated web tool

V. Alexandrov(, U. Lehnert, N. Echols, D. Milburn, D. Engelman and M. Gerstein

Department of Molecular Biophysics and Biochemistry,

Yale University, 266 Whitney Avenue, New Haven, CT 06520, USA

Abstract.  We carry out an extensive statistical study of the applicability of normal modes to the prediction of mobile regions in proteins and their probable directions of motions. In particular, we assess the degree to which the direction of the observed motion, described by vectors connecting corresponding atoms of a protein in two conformations, coincides with the displacement vectors of the lowest normal mode for a single one of these conformations. To answer this question, we develop a comprehensive dataset of non-redundant single-domain motions, model the motions with normal modes, and calculate directional overlap statistics.  Our study suggests that it is possible to extract information from the lowest frequency mode indicating which parts of a protein move most (i.e. have the largest amplitudes) and in which direction. Based on our findings, we have developed a web tool (available at http://molmovdb.org/nma) for predicting motions. As representative examples, we apply our tool to the motions in bacteriorhodopsin, calmodulin, insulin and T7 RNA polymerase.

Introduction

In the analysis of protein dynamics, an important goal is the description of slow large-amplitude motions. These motions, while strongly damped, typically describe conformational changes, which are essential for the functioning of proteins. Only global collective motions can change the exposed surface of the protein significantly and hence influence interactions with its environment. Such structural rearrangements in the protein can occur on a local level within a single domain or can involve large movements of protein domains in a multi-domain protein. Protein dynamics thus covers a broad time scale: 10-14 -10 s (Wilcox et al. 1988). However, many large-amplitude conformational changes are not on a time scale accessible by most theoretical methods that are time-dependent, such as phase space sampling techniques (e.g. molecular dynamics). Therefore, in order to gain insights into the mechanism of slow, large-amplitude motions, one must resort to the use of a time-independent approach, such as normal mode analysis (Levitt et al. 1985).

Normal Mode Analysis (NMA) is a fast and simple method to calculate vibrational modes and protein flexibility. In NMA, sometimes restrained to C atoms only, the atoms are modeled as point masses, connected by springs, which represent the interatomic force fields. One particular type of NMA is the elastic network model. In this model, the springs connecting each node to all other neighboring nodes are of equal strength and only the atom pairs within a cutoff distance are considered.

All existing NMA techniques have important common limitations resulting from the use of the harmonic approximation, the neglect of solvent damping and the absence of information about energy barriers and multiple minima on the potential energy surface (conformational substates accessible by thermal fluctuations (Elber and Karplus 1987; Frauenfelder et al. 1988; Hong et al. 1990). In fact, the most interesting, biologically significant low-frequency motions in a realistic environment are overdamped and hence not vibrational at all, rendering the corresponding normal mode frequencies of little physical significance (Go et al. 1983; Kottalam and Case 1990; Horiuchi and Go 1991; Amadei et al. 1993). Therefore, the identification and characterization of low-frequency domain motions by using NMA might seem questionable. Nevertheless, comparisons of low-frequency normal modes and the directions of large-amplitude fluctuations in molecular dynamics simulations indicate clear similarities (Amadei et al. 1993; Hayward et al. 1997). In particular, close directional coincidence of the lowest normal mode axes and the first principal component axes obtained from molecular dynamic simulations has been observed (Hayward et al. 1997). In addition, the axes of the first modes were found to be overwhelmingly closure axes. A lesser degree of correspondence was observed for the second modes.

It has also been shown that the low-frequency modes describing the large-scale real-world motions of a protein can be related to its fundamental biological characteristics (Brooks and Karplus 1985; Thomas A 1999). For example, Bahar and Jernigan (Bahar and Jernigan 1998) successfully analyzed the vibrational dynamics of transfer RNAs, both free and complexed with the cognate synthetase using the elastic network model. The authors examined the global mode of motion of tRNAGln complexed with glutaminyl-tRNA synthetase and established that certain residues that cluster near the ATP binding site, form a hinge-bending region controlling the cooperative motion, and thereby the catalytic function of the enzyme. Normal modes have been successfully used to display concerted motions of proteins (Noguti and Go 1982; Brooks and Karplus 1983; Go et al. 1983; Levy et al. 1984; Levitt et al. 1985; Henry et al. 1986), including slow motions between protein domains as in the hinge-bending motion of lysozyme (Brooks and Karplus 1985; Gibrat and Go 1990). Recently, Valadie et al (Valadie et al. 2003) showed that the first step of the gating mechanism in mechanosensitive channel (MscL) can be described with only the three lowest-frequency modes. Their results clearly indicate that the movement associated to these modes is an iris-like movement involving both tilts and twists. Several other works showed that low frequency modes overlap with real conformational changes (Thomas A 1999; Tama and Sanejouand 2001). There is also evidence to suggest that proper, symmetric normal mode vibration of binding pockets is crucial to correct biological activity in some proteins (Marques 1995; Thomas A 1996a; Thomas A 1996b; Hinsen 1998; Miller 1999).

Experimental data on protein motions from incoherent neutron scattering, and resulting observations of the density of states were also found to agree with simulations (Smith et al. 1987; Cusack et al. 1988). In particular, inelastic neutron scattering spectra have resolved the density of states of the modes of myoglobin in the low-frequency regime at room temperature (Cusack and Doster 1990). Site-selective fluorescence spectroscopy of Zn-substituted myoglobin has obtained this density without the use of model shape functions (Ahn et al. 1993). Resonance Raman spectra generated by ps laser pulses have also been interpreted by analyzing relaxation of protein normal modes (R. Alden 1992).

Despite the large body of successful NMA applications in protein dynamics studies, both theoretical and experimental, normal modes have only been compared to actual motions on a case-by-case basis. Few analyses have attempted to do this comprehensively in a database framework. Thus, the need for statistical assessment of the overall reliability and applicability of NMA to the description of various aspects of protein motion becomes apparent. In our previous work (Krebs et al. 2002) we performed a large-scale database study of molecular motions within the MolMovDB (Gerstein and Krebs 1998; Krebs and Gerstein 2000; Echols et al. 2003) framework. The results indicated that the lowest frequency normal mode contributes the most to the decomposition of the real (observed) motion in a linear combination of the first twenty normal modes, in agreement with the findings mentioned above. In the present work, we ask to what degree the direction of the observed motion, described by vectors connecting corresponding atoms of a protein in its initial and final conformation, coincides with the displacement vectors of the lowest normal modes for the initial conformation. Since structure pairs may not always be available, the other main motivation behind this work was to develop an easy-to-use motion prediction technique capable of assessing the direction of the actual protein motion.

Therefore, we constructed a comprehensive set of observed  non-redundant molecular motions, which we used to assess the quality of NMA predictions. If structures of two alternative conformations (one assigned to be “initial“ and the other “final“) are known, a direct comparison can be done between the difference vector of the two conformations and the calculated displacement vector of the lowest normal mode. Our results suggest that the top 2-3% of the most significant inter-domain movements in a protein can nevertheless be modeled successfully by a set of the corresponding lowest normal mode displacement vectors. We developed ab-initio selection criteria based on either indirect experimental evidence (B-factors) or structural variability within the corresponding fold family (in the multiple structural alignment sense) to single out those NMA displacement vectors that accurately model the most mobile parts of the molecule. Since portions of the molecule moving the most usually represent the most “biologically interesting” parts in a protein and normally serve as an approximate description of the overall motion, the goal to obtain a fast qualitative prediction of the overall motion has been achieved.

Results and Discussion

Constructing a new Set of non-redundant motions

The set of all chain sequences (~33,000 entries) extracted from all crystallographically determined proteins deposited in the PDB was a subject to all-vs-all sequence alignment using the FASTA program (Pearson and Lipman 1988). The pairs with greater than 99% identity (~700,000 pairs) were selected for the initial pool of tentative motions. Structural alignment for this set of tentative structure pairs was performed using LSQ (Least Square Fit) method to select pairs with RMSD (Root-Mean-Squared Deviation) greater than 1.5 Å. To achieve an optimal superposition of the two structures we used our in-house structural alignment routine, which finds the solution for the parameters of the RMSD-minimizing rotation matrix (RM) as suggested by Kabsch (Kabsch. 1976). This RMSD value was used to select the final (comprehensive) set of structures within the chosen RMSD cutoff of 1.5 Å.

In this comprehensive set of 13,571 structure pairs, 11,217 were successfully “morphed”, i.e. a motion pathway could be constructed by the morph server.  From those, 7467 were located in the CATH database (Orengo 1997) by their PDB and chain identifiers (Fig. 2). Morphs falling into the same near-identical CATH level (defined as all sequences with 99% identity) were taken and examined collectively to identify a single best representative morph. Where possible, structure pairs with one domain missing were discarded, and the groupings were further reduced by taking only those pairs with sequence length greater than the mean for each set, thus eliminating truncated proteins. Finally, the morph with median overall RMSD between the initial and final frames was selected as the representative entry. In those families where the set was too small to perform this procedure, the morph with highest RMSD (and in some cases, the only available morph) was selected by default.  Thus the final (non-redundant) set of 377 morphs had no more than 95% sequence identity between any two entries. These morphs, in the context of the overall CATH schema, are viewable at http://molmovdb.org/nma

We calculated a histogram of RMSD values for our new non-redundant set of motion pairs (Fig. 3). It shows that more than 90% of the RMSD values lie in the 1.5 – 5.5 Å interval.

Statistical analysis of NMA directional correlations with observed motions

We used an average correlation cosine squared, which we further refer to as S-statistic (Eq. (4)), as an overall quantitative measure of the NMA predicted motions. This quantity simply reflects the degree of average directional similarity between the observed motion vectors and the normal mode displacement vectors. The larger values of S correspond to the lower average angle between the two sets of vectors.

First, we calculated the value of S and S2 for each motion pair in our data set, and plotted histograms of these values (Fig. 4 and 5). S2 statistic appears to be useful because the corresponding values of the average angle are mapped more uniformly to the interval [0..1]. To get a rough estimate of the average value for the directional overlap, assume that all atoms in a structure pair have a similar overlap . Then the peak (most common) value 0.48 of S2 in the histogram would imply (see Eq. (4)) an average angle  of 51 degrees, the angle between a typical normal mode displacement vector and an actual motion vector for the same C. This average value of  only marginally differs from the value of 54.7 degrees (Arfken and Weber 2000) between a pair of randomly generated 3D vectors.

The behavior of the S-statistic was also studied as a function of the percentage of the selected Cs. Cs were selected based upon the length of the vector representing the actual movement of that particular C. S-statistics were calculated again for the selected atoms. The histograms for the  and  (S values calculated for the 10% and 2.5% of the most moving Cs, respectively) are shown on Figure 4. The average value of both  and  shifts to the right ( has no real peak anymore). The same trend (higher values of S for fewer selected atoms) can be seen on Figure 5, where S is plotted as a function the percent of selected atoms. These results suggest that the direction of motion is predicted most accurately for C atoms that move the most.

Conveniently, these are the atoms we are most interested in, because just a few such atoms are needed to give an idea what the overall protein motion looks like. We propose that NMA (or at least the lowest frequency mode) is not suitable for providing accurate details for all of the constituent atoms in a biological system, but has a selective accuracy in capturing the large, concerted motion features of a given macromolecule.

Representative examples of correlations with observed motions

Here we describe several examples we have chosen from our comprehensive set, typical representatives of different major classes of motions, to illustrate our approach. In particular, we picked a small fragment shear motion (insulin), a small domain shear motion (bacteriorhodopsin), domain hinge motion (calmodulin) and a large-scale multi-domain refolding motion (T7 polymerase), for which both initial and final conformations are experimentally available (Yin and Steitz 2002). S-values for these motions are plotted on Figure 5. One can see that except for T7, the S value for all the individual structures exhibit consistent performance as the overall 377 single-domain set with regard to selection. Predicted directions of motion for the four most mobile Cs for these motions are shown on Figures 6a-6d. In all cases, the predicted largest movement and the observed one superpose well. They involve the same atoms and point in “similar” direction. These predictions appear to be very helpful in deducing plausible mechanism of protein function.

(i) Insulin. In figure 6a we show the predicted motions of insulin. The first and foremost conclusion of structural studies of insulin is that the protein is extremely flexible and adaptable. Numerous crystal forms depending on their specific T and R conformations are known (Chothia et al. 1983; Hua et al. 1991; Hawkins et al. 1994; Hawkins et al. 1995; Ye et al. 1996; Bao et al. 1997; Whittingham et al. 1997; Schlein et al. 2000; Ye et al. 2001; Dupradeau et al. 2002). The flexibility is especially marked in the B chain: the conformation of the N-terminus gives rise to the T and R naming system, and the flexibility of the C-terminus is thought to be very important in a conformational change necessary for receptor binding. In figure 6a, the vectors representing our predicted motion of insulin suggest that chain B is indeed quite mobile: all significant motion vectors are located in chain B. Furthermore, the vector of motion at residue PHE 1B pointing along the helix axes suggests that this whole helix participates in a concerted motion. The other three vectors in the hinge region (PRO 28B, LYS 29B and ALA 30B) pointing in almost perpendicular direction to the first vector, suggest the motion of chain B is a small fragment shear motion. This result relates to the experimental evidence that the beta-turn motion in chain B (residues B24-B30) is essential for the enzymatic activity of insulin (Bao et al. 1997).

(ii) Calmodulin. Figure 6b shows the predicted movement of calmodulin, a ubiquitous eukaryotic Ca2+-binding protein that participates in numerous cellular regulatory processes. The X-ray structure (Babu et al. 1985; Kretsinger et al. 1986; Babu et al. 1987; 1988) of this highly conserved 148-residue protein has a dumbbell-like shape in which two globular domains are connected by a seven-turn -helix. The binding of Ca2+ to either domain induces a conformational change in that domain, which further induces some other catalytic activity (such as activation of phosphorylase kinase). Much effort was put into determining the details of calmodulin structure and the mechanism of its Ca2+-induced conformational change (Kretsinger et al. 1986; Sekharudu and Sundaralingam 1993; Cook et al. 1994; Chin et al. 1997; Wilson and Brunger 2000; Kurokawa et al. 2001; Han et al. 2002; Hoelz et al. 2003; Yamauchi et al. 2003). The results of our calculations help to interpret the available experimental data. The vectors of the predicted largest moving parts of the molecule (Figure 6b) indicate the direction along which EF-hand is most likely to move. This movement, in agreement with the existing experimental evidence (Persechini and Kretsinger 1988; Reuland et al. 2003), also suggests that calmodulin’s central helix serves as a flexible rather than as a rigid spacer, a property that probably further increases the range of target sequences to which calmodulin can bind (Putkey et al. 1988).

(iii) Bacteriorhodopsin. Bacteriorhodopsin undergoes conformational changes during its catalytic cycle. These conformational changes are mainly restricted to the cytoplasmic side of helices E, F and G and represent a crucial step in the activity of the native protein (Luecke et al. 1999; Subramaniam et al. 1999; Sass et al. 2000). The largest predicted motions in bacteriorhodopsin are shown in Figure 6c. We observe the largest movements for residues VAL101 (helix G), PHE153 (helix E) and VAL177 (helix F). The fact that the ends of the corresponding helices E, G and F, G move towards each other has a biological implication that this movement is a driving force that makes bacteriorhodopsin function as a proton pump. Our prediction of the described movements of helices E, F and G correlates well with the experimentally observed structural changes related to the functional activity of bacteriorhodopsin (Luecke et al. 1999; Subramaniam et al. 1999; Luecke 2000).

(iv) T7 Polymerase.  Studies of Bacteriophage T7 RNA polymerase reaction are crucial in the fundamental understanding of the mechanism of transcription (Jia and Patel 1997a; b), and are also important in biotechnology development (Roe et al. 1988; Majumdar et al. 1989). The high efficiency of T7 RNAP makes it a widely used tool in producing RNA in vitro and microarray gene expression. The motion of T7 RNA polymerase is one of the largest recorded motions in the MolMovDB by any set of criteria. It involves partial refolding of about 250 residues in the N-terminal domain in order to unbind the promoter and open up an exit channel for the nascent RNA (Yin and Steitz 2002). Conformational changes this large are not unheard of (e.g. fusion-triggering conformational change of a fusion domain from influenza hemagglutinin (Bullough et al. 1994; Han et al. 2001)). Still, a motion of this size is quite unexpected for a polymerase that is in the act of transcribing RNA. There is a good chance that additional intermediate stages exist (Yin and Steitz 2003). The normal mode characteristics of the motion for this large multi-domain protein differ significantly from the single-domain motions both in terms of the magnitudes of the displacement vectors and statistical characteristics. For the three single-domain proteins mentioned above, the S-statistic exhibits the same behavior as the one calculated for the whole data set, i.e., S reaches its maximal values (minimal average ) for those atoms that move the most. It turns out that a restricted C selection based on anticipated motion magnitude is not necessary for T7 polymerase. Moreover, for T7 polymerase, NMA predicts the direction of movement for all Cs with slightly greater accuracy compared to the predictions for 2.5% the C’s with the largest motions in our single-domain motion set. This probably happens because the employed NMA allows one to see only the most prominent details of motion, that are better distinguished in a concerted multi-domain movement rather than in a smaller fragment motion. Recently (Cui et al. 2004) determined that “the character of the lowest-frequency modes of the beta(E) subunit is highly correlated with the large beta(E) to beta(TP) transition”, which is in agreement with our findings. However, more experimental data is needed to prove if NMA is better suited for larger motions.

Selection criteria for single-structure predictions

The above analysis suggests that the information about the protein motion contained in the lowest frequency normal mode vectors can be divided onto two parts: (i) the part related to the large-amplitude concerted motion and (ii) the smaller scale part related to local “jittering”. We can exclude the latter part if we restrict our attention to the atoms that move the most.

It becomes apparent that additional criteria are necessary to ensure a reliable prediction of the largest motions when only one conformation is available. The ability to predict atoms that move the most as well as the directions of their motion can be very useful for gaining further insight about the mechanism of protein function in cases where conformational changes are unknown or where no high resolution structures exist.

In general, Cs with large motions can not be reliably selected based on the calculated NMA amplitudes – the correlation coefficient between the sets of normal mode displacements and the corresponding real motion vectors in our data set turns out to be only 0.34. Therefore, we used B-factors to select the Cs with the largest motion vectors. The correlation coefficient calculated for the B-factors versus observed motion amplitudes averaged over our data set appeared to be 0.77. So, when predicting the direction of motion, we are guaranteed, on average, to have seven or eight out of ten atoms that move the most in our NMA description of the real motion based on a B-factor selection criterion. When B-factors for a particular structure are not available, one can select the Cs that move the most based on their structural variation in the multiple structural alignment for the corresponding fold family. In our study, we built multiple structural alignments for every motion pair in our data set in the following way. For each initial conformation, ten structures (if available) were selected from the corresponding fold family. The structures were aligned in such a way, so as to minimize the average RMSD value among all ten structures, in the same way as we did in our previous work (Alexandrov 2004) for calculation of the average core structures for protein fold families. The C consensus positions with the largest structural deviation are assumed to represent the positions that move the most in the observed motion of the original structure. The correlation coefficient between the positional variations and the observed motion amplitudes averaged among all Cs in the data set was found to be 0.83. Thus, the core structures can serve as an independent reliable criterion for selecting the most mobile atoms in a protein family and, particularly, for NMA predictions of directions of motions.

Results of single structure predictions from testing and training data

Since the number of proteins in our non-redundant set of motions is limited, we refined the cut-off value for our S-statistic by using 10-fold cross-validation. The data set of 377 proteins was split into ten equally balanced subsets, each containing ~38 structures from the original set. Structures in each subset were selected completely randomly. Each structure belonged to only a single subset, and there were no duplicated structures in any subset. The optimal value for the cut-off, which turned out to be 2.5%, has been determined in each subset based on the remaining ~340 structures that belonged to the other nine subsets.

In practice, selecting four atoms based on their B-factors for a single structure is sufficient to satisfy this threshold requirement as well as to build an overall qualitative picture of the overall protein motion. Motion prediction based on only a single “best” atom selection is also a viable alternative. The distribution of average absolute angles  based on the one-atom  and four-atom  largest B-factor selection criteria for the entire data set is shown on Figure 7. Both distributions appear to be very similar. One can see from the figure that accurate motion direction predictions (<30 degrees deviation from the observed direction) occur commonly but not all the time. This is expected, however. NMA, in general, is not a very accurate description of the real-life motion. In addition, the longest trajectory in a protein motion is rarely a straight line. Therefore, an otherwise correctly predicted initial direction of motion (NMA prediction) might deviate noticeably from the vector connecting its initial and final positions. This suggests, in turn, that a picture represented by four atoms with the largest B-factors tends to be a better visual description of the overall motion, particularly, in cases involving hinge motion or large-domain motion (from a statistical point of view, however, both one-atom and four-atom motion descriptions are nearly equivalent, since they both satisfy the 2.5% selection criterion).

Implementation of working prediction server

We have set up an NMA web tool at http://molmovdb.org//nma/ to illustrate the main findings in the paper and to provide a motion-prediction service to the community (Figure 8). The tool allows a researcher to identify the key residues involved in the motion and their most probable direction. Given either a PDB/SCOP ID or an uploaded structure (Figure 8a), the server calculates the lowest normal mode of the submitted query, finds and highlights the most mobile structural regions and shows the direction of the four C atoms that move the most (Figure 8b). Selection of the four most accurate NMA vectors is based on either supplied B-factors or the pre-built multiple structural alignment for the corresponding fold family. The four selected atoms are shown in red in the calculated lowest-frequency-normal-mode movie. A static picture with all residues ranked and highlighted based on their motion amplitudes (red color designating the largest motion, and blue - the smallest) is also provided (Figure 8b).

### Conclusion

An extensive statistical study applicability of Normal Modes Analysis to prediction of protein flexibility has been performed on a new, comprehensive dataset of non-redundant single-domain motions. The motions were modeled by using the lowest frequency normal mode and predictions were assessed by directional overlap statistics. Our results suggest that it is possible to extract information from the lowest frequency normal mode, which identifies the most mobile parts of the protein as well as their directions by focusing on a few C atoms that move the most. We propose that the lowest frequency NMA can selectively predict the atoms and the direction of conformational changes occurring in proteins. While the normal mode analysis is based on finding vibrations that do not actually occur in the over-damped condition of a protein in its environment, it appears to usefully indicate the propensity of the structure to change in a particular direction. We find that motion prediction gains reliability if additional criteria, such as crystallographic B-factors and RMSD values from multiple structural alignments, are built in the motion analysis. A web tool for prediction of protein motion and flexibility has been developed to demonstrate the described approach.

Materials and Methods

Basic NMA framework and its MMTK implementation

The concept of Normal Mode Analysis is to find a set of basis vectors (normal modes) describing the molecule's concerted atomic motion and spanning the set of all  degrees of freedom. For very large molecules, it is often of more interest to find a small subset of these normal modes that seem in some way especially important. By modeling the inter-atomic bonds as springs and analyzing the protein as a large set of coupled harmonic oscillators, one can calculate a frequency of periodic motion associated with each normal mode, and then attempt to find normal modes with low frequencies.

The principal of normal mode analysis is to solve an eigenvalue equation of the form

(1)

where q is a vector representing the displacements in three dimensions of the various atoms of the molecule, and F is a matrix that can be computed from the mass of the system and potential energy functions. Solutions to the above system are vectors of periodic functions (the normal modes) vibrating in unison at the characteristic frequency of the mode.

We used MMTK (Hinsen 2000) to carry out Normal Mode Analysis on pre-processed PDB file pairs containing only C( coordinates. The numerical Python module (Ascher et al. 2000) was employed to carry out all linear algebra computations.  Each residue was approximated as a single virtual atom with mass of the corresponding amino acid and centered at its C( coordinate. The MMTK deformation force field was used to model inter-atomic C( interactions. In this model, the energy is computed as the difference between a displaced model and the experimental structure using the formula:

,	(2)

where is a constant, is the vector connecting atom i to atom j in the experimental structure, is the difference vector between atom i in the displaced (final) structure and the same atom in the initial structure. Furthermore, in the practical implementation of the NMA used here (Hinsen 2000), the force constant value decreases with distance as an exponential function to allow its efficient evaluation with a cutoff not significantly larger then the interatomic equilibrium distance .

In order to accelerate our computations, we restricted MMTK to compute only the twenty lowest-frequency normal modes. In our earlier work (Krebs et al. 2002) we showed that this truncation is adequate for qualitative characterization of the lowest frequency protein motions.

Statistical measures for assessing overlap

A means of quantifying the similarity of the displacement between the PDB structures and the normal mode displacement vectors can be achieved in terms of the following quantities

(3)

In the above formula, we define the ‘directional overlap’  for one particular atom i as the absolute value of cosine of the angle between the displacement vector  of the lowest frequency mode and the observed direction of motion  (Fig. 1).

We use these individual directional overlaps  to define the second order statistic, S-statistic:

,					(4)

which serves as an overall quantitative measure of the similarity in directionality between the observed motion vectors and the normal mode displacement vectors.

We also define an overlap measure in relation to atom selection. The quantity  is defined as

,						(5)

where the sum is carried over the first P percent of Cs with the largest difference vectors  (). When the number of selected atoms is small, it is convenient to rewrite the quantity as

, 						(6)

in order to explicitly indicate the number M of Cs with the largest difference vectors entering the sum in Eqs. (5) and (6). Quantities  and  are defined in exactly the same way as their counterparts  and  except that the selection of Cs is carried with respect to their corresponding B-factors, rather than the difference vectors.

For robustness, we can also define an average angle

,					(7)

where summation is carried over N<M angles corresponding to the C atoms with the largest B-factors.

Figure legends.

Figure 1. Notations used in the paper. Rij is the vector connecting atom i to atom j in the experimental (initial) structure; j is the difference vector between atom i in the displaced (final) structure and the same atom in the initial structure; Dj is the lowest normal mode displacement vector for atom j in the initial conformation; j is the angle between vectors Dj and j for atom j.

Figure 2. An illustration of the scheme that was used to identify data set of non-redundant domain motions

Figure 3. Distribution of RMSD scores (in Angstroms) for the non-redundant set of domain motions.

Figure 4. Histogram of S2 statistic and the corresponding average j angle values for 100% (dotted), 10% (dashed) and  2.5% (solid) selected C based on the motion amplitudes in the non-redundant data set of domain motions. Selection of the most moving atoms results in larger values of S2 (the larger values of S and S2 correspond to the lower average angle between the two sets of vectors). Dotted line points to the location of j  equal to 54.7°, the average angle between two randomly generated vectors.

Figure 5. S statistic as a function of percentage of the largest selected C displacements for single-domain and multi-domain protein motions

Figure 6a. Real motion (red) and NMA-predicted (blue) vectors for the motion of insulin (d7insb_ SCOP domain). The arrows indicate just the directions of motion.

Figure 6b. Real motion (red) and NMA-predicted (blue) vectors for the motion of calmodulin (d2bbm__ domain). The arrows indicate just the directions of motion.

Figure 6c. Real motion (red) and NMA-predicted (blue) vectors for the motion of bacteriorhodopsin (d1c8sa_ SCOP domain). The arrows indicate just the directions of motion.

Figure 6d. Real motion (red) and NMA-predicted (blue) vectors for the motion of T7 polymerase (elongation complex). Labels 1,2,3 and 4 represent residues THR 596, VAL 597, THR 598 and GLY 603 respectively. The arrows indicate just the directions of motion.

Figure 7. Histogram of the average angle between the lowest frequency normal mode vectors and the corresponding observed displacement vectors for the selected C with the largest B-factors in the non-redundant data set of domain motions.  distribution is represented by the solid line, and  by the dashed line.

Figure 8a. NMA motion and flexibility prediction server: input page.

Figure 8b. NMA motion and flexibility prediction server: results page

References

Ahn, J.S., Kanematsu, Y., and Kushida, T. 1993. Site-selective fluorescence spectroscopy in dye-doped polymers. I. Determination of the site-energy distribution and the single-site fluorescence spectrum. Physical Review. B. Condensed Matter. 48: 9058-9065.

Alexandrov, V., and Gerstein, M. 2004. Using 3D Hidden Markov Models that explicitly represent spatial coordinates to model and compare protein structures. BMC Bioinformatics 5:2.

Amadei, A., Linssen, A.B., and Berendsen, H.J. 1993. Essential dynamics of proteins. Proteins 17: 412-425.

Arfken, G.B., and Weber, H. 2000. Mathematical Methods for Physicists. Academic Press.

Ascher, D., Dubois, P.F., Hinsen, K., Hugunin, J., and Oliphant, T. 2000. Numerical Python. Lawrence Livermore National Laboratory, Livermore, CA 94566.

Babu, Y.S., Bugg, C.E., and Cook, W.J. 1987. X-ray diffraction studies of calmodulin. Methods Enzymol 139: 632-642.

Babu, Y.S., Bugg, C.E., and Cook, W.J. 1988. Structure of calmodulin refined at 2.2 A resolution. J Mol Biol 204: 191-204.

Babu, Y.S., Sack, J.S., Greenhough, T.J., Bugg, C.E., Means, A.R., and Cook, W.J. 1985. Three-dimensional structure of calmodulin. Nature 315: 37-40.

Bahar, I., and Jernigan, R.L. 1998. Vibrational dynamics of transfer RNAs: comparison of the free and synthetase-bound forms. J Mol Biol 281: 871-884.

Bao, S.J., Xie, D.L., Zhang, J.P., Chang, W.R., and Liang, D.C. 1997. Crystal structure of desheptapeptide(B24-B30)insulin at 1.6 A resolution: implications for receptor binding. Proc Natl Acad Sci U S A 94: 2975-2980.

Brooks, B., and Karplus, M. 1983. Harmonic dynamics of proteins: normal modes and fluctuations in bovine pancreatic trypsin inhibitor. Proc Natl Acad Sci U S A 80: 6571-6575.

Brooks, B., and Karplus, M. 1985. Normal modes for specific motions of macromolecules: application to the hinge-bending mode of lysozyme. Proc Natl Acad Sci U S A 82: 4995-4999.

Bullough, P.A., Hughson, F.M., Skehel, J.J., and Wiley, D.C. 1994. Structure of influenza haemagglutinin at the pH of membrane fusion. Nature 371: 37-43.

Chin, D., Winkler, K.E., and Means, A.R. 1997. Characterization of substrate phosphorylation and use of calmodulin mutants to address implications from the enzyme crystal structure of calmodulin-dependent protein kinase I. J Biol Chem 272: 31235-31240.

Chothia, C., Lesk, A.M., Dodson, G.G., and Hodgkin, D.C. 1983. Transmission of conformational change in insulin. Nature 302: 500-505.

Cook, W.J., Walter, L.J., and Walter, M.R. 1994. Drug binding by calmodulin: crystal structure of a calmodulin-trifluoperazine complex. Biochemistry 33: 15259-15265.

Cui, Q., Li, G., Ma, J., and Karplus, M. 2004. A normal mode analysis of structural plasticity in the biomolecular motor F(1)-ATPase. J Mol Biol 340: 345-372.

Cusack, S., and Doster, W. 1990. Temperature dependence of the low frequency dynamics of myoglobin. Measurement of the vibrational frequency distribution by inelastic neutron scattering. Biophys J 58: 243-251.

Cusack, S., Smith, J., Finney, J., Tidor, B., and Karplus, M. 1988. Inelastic neutron scattering analysis of picosecond internal protein dynamics. Comparison of harmonic theory with experiment. J Mol Biol 202: 903-908.

Dupradeau, F.Y., Richard, T., Le Flem, G., Oulyadi, H., Prigent, Y., and Monti, J.P. 2002. A new B-chain mutant of insulin: comparison with the insulin crystal structure and role of sulfonate groups in the B-chain structure. J Pept Res 60: 56-64.

Echols, N., Milburn, D., and Gerstein, M. 2003. MolMovDB: analysis and visualization of conformational change and structural flexibility. Nucleic Acids Res 31: 478-482.

Elber, R., and Karplus, M. 1987. Multiple conformational states of proteins: a molecular dynamics analysis of myoglobin. Science 235: 318-321.

Frauenfelder, H., Parak, F., and Young, R.D. 1988. Conformational substates in proteins. Annu Rev Biophys Biophys Chem 17: 451-479.

Gerstein, M., and Krebs, W. 1998. A database of macromolecular motions. Nucleic Acids Res 26: 4280-4290.

Gibrat, J.F., and Go, N. 1990. Normal mode analysis of human lysozyme: study of the relative motion of the two domains and characterization of the harmonic motion. Proteins 8: 258-279.

Go, N., Noguti, T., and Nishikawa, T. 1983. Dynamics of a small globular protein in terms of low-frequency vibrational modes. Proc Natl Acad Sci U S A 80: 3696-3700.

Han, B.G., Han, M., Sui, H., Yaswen, P., Walian, P.J., and Jap, B.K. 2002. Crystal structure of human calmodulin-like protein: insights into its functional role. FEBS Lett 521: 24-30.

Han, X., Bushweller, J.H., Cafiso, D.S., and Tamm, L.K. 2001. Membrane structure and fusion-triggering conformational change of the fusion domain from influenza hemagglutinin. Nat Struct Biol 8: 715-720.

Hawkins, B., Cross, K., and Craik, D. 1995. Solution structure of the B-chain of insulin as determined by 1H NMR spectroscopy. Comparison with the crystal structure of the insulin hexamer and with the solution structure of the insulin monomer. Int J Pept Protein Res 46: 424-433.

Hawkins, B.L., Cross, K.J., and Craik, D.J. 1994. A 1H-NMR determination of the solution structure of the A-chain of insulin: comparison with the crystal structure and an examination of the role of solvent. Biochim Biophys Acta 1209: 177-182.

Hayward, S., Kitao, A., and Berendsen, H.J. 1997. Model-free methods of analyzing domain motions in proteins from simulation: a comparison of normal mode analysis and molecular dynamics simulation of lysozyme. Proteins 27: 425-437.

Henry, E.R., Eaton, W.A., and Hochstrasser, R.M. 1986. Molecular dynamics simulations of cooling in laser-excited heme proteins. Proc Natl Acad Sci U S A 83: 8982-8986.

Hinsen, K. 1998. Analysis of domain motions by approximate normal mode calculations. Proteins 33: 417-429.

Hinsen, K. 2000. The Molecular Modeling Toolkit: A New Approach to Molecular Simulations. Journal of Computational Chemistry.

Hoelz, A., Nairn, A.C., and Kuriyan, J. 2003. Crystal structure of a tetradecameric assembly of the association domain of Ca2+/calmodulin-dependent kinase II. Mol Cell 11: 1241-1251.

Hong, M.K., Braunstein, D., Cowen, B.R., Frauenfelder, H., Iben, I.E., Mourant, J.R., Ormos, P., Scholl, R., Schulte, A., Steinbach, P.J., et al. 1990. Conformational substates and motions in myoglobin. External influences on structure and dynamics. Biophys J 58: 429-436.

Horiuchi, T., and Go, N. 1991. Projection of Monte Carlo and molecular dynamics trajectories onto the normal mode axes: human lysozyme. Proteins 10: 106-116.

Hua, Q.X., Shoelson, S.E., Kochoyan, M., and Weiss, M.A. 1991. Receptor binding redefined by a structural switch in a mutant human insulin. Nature 354: 238-241.

Jia, Y., and Patel, S.S. 1997a. Kinetic mechanism of GTP binding and RNA synthesis during transcription initiation by bacteriophage T7 RNA polymerase. J Biol Chem 272: 30147-30153.

Jia, Y., and Patel, S.S. 1997b. Kinetic mechanism of transcription initiation by bacteriophage T7 RNA polymerase. Biochemistry 36: 4223-4232.

Kabsch., W. 1976. Acta Cryst. A32: 922-923.

Kottalam, J., and Case, D.A. 1990. Langevin modes of macromolecules: applications to crambin and DNA hexamers. Biopolymers 29: 1409-1421.

Krebs, W.G., Alexandrov, V., Wilson, C.A., Echols, N., Yu, H., and Gerstein, M. 2002. Normal mode analysis of macromolecular motions in a database framework: developing mode concentration as a useful classifying statistic. Proteins 48: 682-695.

Krebs, W.G., and Gerstein, M. 2000. The morph server: a standardized system for analyzing and visualizing macromolecular motions in a database framework. Nucleic Acids Res 28: 1665-1675.

Kretsinger, R.H., Rudnick, S.E., and Weissman, L.J. 1986. Crystal structure of calmodulin. J Inorg Biochem 28: 289-302.

Kurokawa, H., Osawa, M., Kurihara, H., Katayama, N., Tokumitsu, H., Swindells, M.B., Kainosho, M., and Ikura, M. 2001. Target-induced conformational adaptation of calmodulin revealed by the crystal structure of a complex with nematode Ca(2+)/calmodulin-dependent kinase kinase peptide. J Mol Biol 312: 59-68.

Levitt, M., Sander, C., and Stern, P.S. 1985. Protein normal-mode dynamics: trypsin inhibitor, crambin, ribonuclease and lysozyme. J Mol Biol 181: 423-447.

Levy, R.M., Srinivasan, A.R., Olson, W.K., and McCammon, J.A. 1984. Quasi-harmonic method for studying very low frequency modes in proteins. Biopolymers 23: 1099-1112.

Luecke, H. 2000. Atomic resolution structures of bacteriorhodopsin photocycle intermediates: the role of discrete water molecules in the function of this light-driven ion pump. Biochim Biophys Acta 1460: 133-156.

Luecke, H., Schobert, B., Richter, H.T., Cartailler, J.P., and Lanyi, J.K. 1999. Structural changes in bacteriorhodopsin during ion transport at 2 angstrom resolution. Science 286: 255-261.

Majumdar, D., Lieberman, K.R., and Wyche, J.H. 1989. Use of modified T7 DNA polymerase in low melting point agarose for DNA gap filling and molecular cloning. Biotechniques 7: 188-191.

Marques, O.a.S., Y. H. 1995. Hinge-bending motion in citrate synthase arising from normal mode calculations. Proteins 23: 557-560.

Miller, D.W.a.A., D. A. 1999. Enzyme specificity under dynamic control: a normal mode analysis of alpha-lytic protease. Journal of Molecular Biology 286: 267-278.

Noguti, T., and Go, N. 1982. Collective variable description of small-amplitude conformational fluctuations in a globular protein. Nature 296: 776-778.

Orengo, C.A., Michie, A.D., Jones, S., Jones, D.T., Swindells, M.B., and Thornton, J. M. 1997. CATH- A Hierarchic Classification of Protein Domain Structures. Structure 5: 1093-1108.

Pearson, W.R., and Lipman, D.J. 1988. Improved tools for biological sequence comparison. Proc Natl Acad Sci U S A 85: 2444-2448.

Persechini, A., and Kretsinger, R.H. 1988. The central helix of calmodulin functions as a flexible tether. J Biol Chem 263: 12175-12178.

Putkey, J.A., Ono, T., VanBerkum, M.F., and Means, A.R. 1988. Functional significance of the central helix in calmodulin. J Biol Chem 263: 11242-11249.

R. Alden, M.S., M. Ondrias, S. Courtney, and J. Friedman. 1992. J. Raman Spectrosc. 23.

Reuland, S.N., Vlasov, A.P., and Krupenko, S.A. 2003. Disruption of a calmodulin central helix-like region of 10-formyltetrahydrofolate dehydrogenase impairs its dehydrogenase activity by uncoupling the functional domains. J Biol Chem 278: 22894-22900.

Roe, B.A., Johnston-Dow, L., and Mardis, E. 1988. Use of a chemically modified T7 DNA polymerase for manual and automated sequencing of supercoiled DNA. Biotechniques 6: 520.

Sass, H.J., Buldt, G., Gessenich, R., Hehn, D., Neff, D., Schlesinger, R., Berendzen, J., and Ormos, P. 2000. Structural alterations for proton translocation in the M state of wild-type bacteriorhodopsin. Nature 406: 649-653.

Schlein, M., Havelund, S., Kristensen, C., Dunn, M.F., and Kaarsholm, N.C. 2000. Ligand-induced conformational change in the minimized insulin receptor. J Mol Biol 303: 161-169.

Sekharudu, C.Y., and Sundaralingam, M. 1993. A model for the calmodulin-peptide complex based on the troponin C crystal packing and its similarity to the NMR structure of the calmodulin-myosin light chain kinase peptide complex. Protein Sci 2: 620-625.

Smith, J., Cusack, S., Poole, P., and Finney, J. 1987. Direct measurement of hydration-related dynamic changes in lysozyme using inelastic neutron scattering spectroscopy. J Biomol Struct Dyn 4: 583-588.

Subramaniam, S., Lindahl, M., Bullough, P., Faruqi, A.R., Tittor, J., Oesterhelt, D., Brown, L., Lanyi, J., and Henderson, R. 1999. Protein conformational changes in the bacteriorhodopsin photocycle. J Mol Biol 287: 145-161.

Tama, F., and Sanejouand, Y.H. 2001. Conformational change of proteins arising from normal mode calculations. Protein Eng 14: 1-6.

Thomas A, F.M.J., Mouawad L. and Perahia D. 1996a. Analysis of the low frequency normal modes of the T-state of aspartate transcarbamylase. Journal of Molecular Biology 257: 1070-1087.

Thomas A, F.M.J.a.P.D. 1996b. Analysis of the low-frequency normal modes of the R state of aspartate transcarbamylase and a comparison with the T state modes. Journal of Molecular Biology 261: 490-506.

Thomas A, H.K., Field M. J, Perahia D. 1999. Tertiary and quaternary conformational changes in aspartate transcarbamylase: a normal mode study. Proteins 34: 96-112.

Valadie, H., Lacapcre, J.J., Sanejouand, Y.H., and Etchebest, C. 2003. Dynamical properties of the MscL of Escherichia coli: a normal mode analysis. J Mol Biol 332: 657-674.

Whittingham, J.L., Havelund, S., and Jonassen, I. 1997. Crystal structure of a prolonged-acting insulin with albumin-binding properties. Biochemistry 36: 2826-2831.

Wilcox, G.L., Quiocho, F.A., Levinthal, C., Harvey, S.C., Maggiora, G.M., and McCammon, J.A. 1988. Symposium overview. Minnesota Conference on Supercomputing in Biology: Proteins, Nucleic Acids, and Water. J Comput Aided Mol Des 1: 271-281.

Wilson, M.A., and Brunger, A.T. 2000. The 1.0 A crystal structure of Ca(2+)-bound calmodulin: an analysis of disorder and implications for functionally relevant plasticity. J Mol Biol 301: 1237-1256.

Yamauchi, E., Nakatsu, T., Matsubara, M., Kato, H., and Taniguchi, H. 2003. Crystal structure of a MARCKS peptide containing the calmodulin-binding domain in complex with Ca2+-calmodulin. Nat Struct Biol 10: 226-231.

Ye, J., Chang, W., and Liang, D. 2001. Crystal structure of destripeptide (B28-B30) insulin: implications for insulin dissociation. Biochim Biophys Acta 1547: 18-25.

Ye, S., Wan, Z., Liu, C., Chang, W., and Liang, D. 1996. Crystal structure of (L-Arg)-B0 bovine insulin at 0.21 nm resolution. Sci China C Life Sci 39: 465-473.

Yin, Y.W., and Steitz, T.A. 2002. Structural basis for the transition from initiation to elongation transcription in T7 RNA polymerase. Science 298: 1387-1395.

Yin, Y.W., and Steitz, T.A. 2003. Private communication.

# Footnotes

( To whom correspondence should be addressed: nmodes2-paper@bioinfo.mbb.yale.edu